## Slide 1: Radio Altimeter Tolerance of Wireless Avionics Intra-Communication (WAIC) Systems
Joshua Ruff
Advisor: Dr. Gregory H. Huff
Electromagnetics and Microwave Laboratory
Department of Electrical and Computer Engineering, TAMU
College Station, Texas, 77843-3128
3-8-2019

## Slide 2: Radio Altimeter Tolerance of WAIC Systems
This work was sponsored by the Aerospace Vehicles Systems Institute (AVSI) through Authorization for Expenditure 76s1 (AFE 76s1)
Project members include Honeywell, Rockwell Collins, Thales, Airbus, Boeing, Garmin
Members contributed funding, equipment, and expertise without which the project would not have been completed
Members contributed widely used commercial radio altimeter models for testing
Acknowledgements
Project Funding

## Slide 3: Introduction

## Slide 4: Radio Altimeter Tolerance of WAIC Systems
Critical instruments have redundant wiring
Moving to wireless reduces need for redundant paths
Interest in wireless spans the aerospace industry:
  Regulators: dissimilar redundancy
  Airframers: fuel efficiency
  Manufacturers: new products
Introduction
Motivation – Wireless Avionics
Source: https://www.bbc.com/news/business-23076586

## Slide 5: Radio Altimeter Tolerance of WAIC Systems
Feasibility study found no insurmountable barriers
AVSI began effort to acquire spectrum in 2008
Effort to find suitable band spanned World Radio Conferences in 2012 and 2015 (WRC-12 and WRC-15)
  WAIC placed on agenda at WRC-12, studied candidate bands
  An allocation in the Radio Altimeter (4.2-4.4GHz) band was secured at WRC-15
As a condition of allocation, WAIC had to develop international standards which ensured compatibility with radio altimeters
Introduction
History – Acquiring Spectrum

## Slide 6: Radio Altimeter Tolerance of WAIC Systems
AVSI wanted to determine WAIC operating characteristics which ensured compatibility with radio altimeters
Altimeter manufacturers could have done this themselves, but a neutral party provided objectivity
Approached Huff Research Group at Texas A&M to develop an automated test bench for radio altimeters
My contribution was the development of this test bench throughout the project, the execution of these compatibility tests, and support the analysis of the data
Introduction
Project Goals

## Slide 7: Background

## Slide 8: Radio Altimeter Tolerance of WAIC Systems
Radio altimeters (RAs) measure height with radar signal
Function on the 4200 – 4400 MHz band
Used in autopilot, navigation systems
Safety critical function
  Heavily regulated
Background
Radar Altimeter Applications
Image showing altimeter on plane

## Slide 9: Radio Altimeter Tolerance of WAIC Systems
Background
Radar Altimeter Functionality
Frequency Modulated Carrier (FMCW) waveform
Return time of signal proportional to frequency
FMCW diagram from DO-155

## Slide 10: Radio Altimeter Tolerance of WAIC Systems
Background
Altimeter Signal Processing
Block diagram here
Homodyne detection extracts altitude data
Actively transmitted waveform fed into receiver mixer
Down converted to baseband
FFT allows post processing in frequency domain
Proprietary algorithms then estimate altitude

## Slide 11: Radio Altimeter Tolerance of WAIC Systems
Backgound
Loop Loss
Height [ft] | Loop Loss [dB]
40 | 76
95 | 84
500 | 100
1500 | 109
3000 | 116
5000 | 120
8000 | 124
RA signal affected by:
  TX/RX Cable losses
  Free Space Path Loss
  Scattering by Ground
  Antenna gains
Standard loop losses defined in RTCA DO-155
  encapsulates these effects for standard configurations
Loop loss for 60° antennas and worse case scattering

## Slide 12: Test Bed Development

## Slide 13: Radio Altimeter Tolerance of WAIC Systems
Three test regimens
  First developed testbed and investigated basic altimeter response
  Second tested filled entire band with representative interference
  Third tested out of band signals
Results from the first test informed both the second and third studies
Results from next two studies inform regulatory action
Out of band testing still active
  Preliminary results shown here
Test Bed Development
Project Overview

## Slide 14: Radio Altimeter Tolerance of WAIC Systems
Test bed developed from DO-155 specs
Basic test bed required
  Altitude Simulator
  Data Acquisition
Altitude simulator most critical
Device which delays and attenuates RF energy
WAIC Only Interference
Basic Altimeter Test Bed
Basic altimeter test bed from DO-155

## Slide 15: Radio Altimeter Tolerance of WAIC Systems
AVSI developed testbed based on DO-155
VSG coupled to altitude simulator output
Altimeter operates normally
  computed altitude output on digitial avionics bus (ARINC-429)
Copilot software reads data from ARINC bus
WAIC Only Interference
Modified Altimeter Test Bed

## Slide 16: Radio Altimeter Tolerance of WAIC Systems
WAIC Only Interference
Altitude Simulator
ODL implements altitude simulator
Switchable “Fixed” and “Step attenuator” achieve desired loop loss
Cascade different spools of fiber optic line for different altitude

## Slide 17: Radio Altimeter Tolerance of WAIC Systems
WAIC Only Interference
Full Setup Diagram

## Slide 18: Radio Altimeter Tolerance of WAIC Systems
WAIC Only Interference
Waveform Generation
MSK and OFDM used for interference
  OFDM used for LTE
  MSK variant used for GSM networks
  Chipset widely available for other bands
OFDM bandwidths varying from 5 to 80 MHz used for testing
40 MHz OFDM on Spectrum Analyzer

## Slide 19: Radio Altimeter Tolerance of WAIC Systems
WAIC Only Interference
Waveform Generation
Dual and single versions of both waveforms used
Dual waveforms had 20 MHz offset
MSK can be interpreted as minimum bandwidth version of OFDM
Wide bandwidth simulates multiple radios
Dual MSK on Spectrum Analyzer

## Slide 20: Radio Altimeter Tolerance of WAIC Systems
WAIC Only Interference
Interference Generation
VSG baseband generator set modulation
RF Generator set carrier frequency and power
RF toggled ON and OFF
  Increasing power over time
RF OFF allows altimeter to recover
Dual MSK on Spectrum Analyzer
Chart: Time
| 0 | 1 | 2 | 3 | 3.0009999999999999 | 4 | 5 | 6 | 6.0010000000000003 | 7 | 8 | 9 | 9.0009999999999994 | 10 | 11 | 12 | 12.000999999999999 | 13 | 14 | 15 | 15.000999999999999 | 16 | 17 | 18 | 18.001000000000001
Power | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 0 | 3 | 3 | 3 | 3 | 0

## Slide 21: Radio Altimeter Tolerance of WAIC Systems
WAIC Only Interference
Software Architecture
Main loop controls power/modulation stepping
Functions in VSG class construct strings for each command
SCPI.py handles TCP connection
Main loop never touches strings or TCP
SCPI Class Hierarchy

## Slide 22: Radio Altimeter Tolerance of WAIC Systems
SQLite database for data storage
Table of measured heights and interference signals
  Both time stamped
Measurements mapped to VSG state
Full Dataset table allows easy plotting
WAIC Only Interference
Data Storage and Post Processing
Functionality of each Python script as it interacts with SQLite database

## Slide 23: Radio Altimeter Tolerance of WAIC Systems
WAIC Only Interference
Data Display – Height Plots
Example ‘Height Plot’ shown
Altitude signal distorted with increasing power
Eventually altimeter throws NCD
Breaking point defined as 2% error or any NCD

## Slide 24: Radio Altimeter Tolerance of WAIC Systems
Tests run at a ‘nominal height’ based on delay device
  500ft, 1500ft, 40ft, ect.
Altimeter may output from ~490 to ~510 for 500ft test
Real installations calibrate out AID and airfame height
We’re only interested in the error
  absolute height not important, so we don’t calibrate
Correct Height defined as median with no interference
All errors measured from this value
WAIC Only Interference
Nominal Height vs Correct Height

## Slide 25: Radio Altimeter Tolerance of WAIC Systems
WAIC Only Interference
Timing and Synchronization
Several Synchronization issues appeared
Significant improvement from leaving TAMU network
‘wait until’ delay function yielded precise interference durations
Ballard internal clock lagged behind slightly
Height Plot zoomed in on one power level

## Slide 26: Radio Altimeter Tolerance of WAIC Systems
WAIC Only Interference
Data Display – Height Plot Again
Height plots were effective but cluttered
Needed more compact way to display same information

## Slide 27: Radio Altimeter Tolerance of WAIC Systems
WAIC Only Interference
Data Display – Stat Plots
Example ‘Stat Plot’ shown
Easier to read than height plot
Shows all the same information except time
Less useful for debugging

## Slide 28: Initial Test Regimen – WAIC Only Interference

## Slide 29: Radio Altimeter Tolerance of WAIC Systems
Find breaking point for different waveforms
Find sensitivity to
  interference bandwidth
  position in spectrum
  Separation of signal into dual waveforms
Bring results to regulators or develop further tests
WAIC Only Interference
Goals and Test Definition
Test definition for last round of initial tests

## Slide 30: Radio Altimeter Tolerance of WAIC Systems
WAIC Only Interference
Breaking Point Definitions
ARINC 707 standards specify minimum accuracy of +/-2%
AVSI determined early on that WAIC would need to cause an error significantly below this margin
  0.5% settled on as a quarter of the allowable error
  Tolerance from all WAIC radios combined on an aircraft

## Slide 31: Radio Altimeter Tolerance of WAIC Systems
WAIC Only Interference
Results

## Slide 32: Radio Altimeter Tolerance of WAIC Systems
WAIC Only Interference
Results

## Slide 33: Radio Altimeter Tolerance of WAIC Systems
WAIC Only Interference
Results
Summary of results submitted to FSMP. Each data point represents the power level at which an altimeter exceeded 0.5% error

## Slide 34: Radio Altimeter Tolerance of WAIC Systems
Altimeters were most sensitive to wider bandwidth signals
Signals at the band edges had fewer effects
  Band center was the most sensitive to interference
Separation of dual waveforms helped but not consistently
Needed to test altimeters under worst case scenario
  Interference from other altimeters during approach
  Full 200MHz band filled WAIC Interferers
Breaking point under these conditions could be brought to regulators
WAIC Only Interference
Results

## Slide 35: Expanding the Test bed

## Slide 36: Radio Altimeter Tolerance of WAIC Systems
Expanding the Test Bed
Overview
Second VSG enables wider band signals
Simulated altimeter signals also injected
VSG controlled over ethernet
Altitude Simulator modified for lower altitudes and higher interference power

## Slide 37: Radio Altimeter Tolerance of WAIC Systems
Expanding the Test Bed
Adding the Second VSG
Resistive 6dB coupler did not provide enough isolation
Looked into new couplers
Garmin provided circulators for free
Function as isolators when one port has a matched load

## Slide 38: Radio Altimeter Tolerance of WAIC Systems
Simulated other altimeter signals using VCOs
Control voltage changes oscillation frequency
Function generators output triangle voltage waveform
Triangle waveform simulates FMCW
Expanding the Test Bed
Simulating Altimeter Interference
Table of control voltages for all 16 VCOs

## Slide 39: Radio Altimeter Tolerance of WAIC Systems
Expanding the Test Bed
VCO Protection Circuit
Function generators capable of destroying the VCO with wrong setting
Designed and simulated a double ‘clipper’ circuit to protect VCOs
Soldered diodes and resistor into function generator leads

## Slide 40: Radio Altimeter Tolerance of WAIC Systems
Airbus provided landing scenario analysis
Approach at a 3° slope
16 nearest interferers on aircraft modeled
Capable of WAIC and RA emissions
External devices placed at wing tip
Minimize slant range
Expanding the Test Bed
Landing Scenario Geometry
Landing scenario geometry for 16 Nearest Interferers

## Slide 41: Radio Altimeter Tolerance of WAIC Systems
Airbus provided a landing scenario analysis
Internal WAIC devices placed at center of airframe
External devices placed at wing tip
Minimize slant range
Expanding the Test Bed
Landing Scenario Geometry
Landing scenario geometry
Both Images of landing scenario used in ICAO Frequency Spectrum Management Panel Information Paper FSMP-WG08-IP04_WAIC_r1

## Slide 42: Radio Altimeter Tolerance of WAIC Systems
Expanding the Test Bed
Worst Case Landing Scenario
Based on geometry, simulated interference path losses (IPL’s)
  16 nearest aircraft
Worst case interference occurred at 200ft
Setup could only achieve 500 or 100ft
Plot of IPL vs altitude in landing scenario

## Slide 43: Radio Altimeter Tolerance of WAIC Systems
Expanding the Test Bed
Connecting VCO Signals
VCOs connected using splitters, programmable attenuator
First two VCOs simulate “Own Ship” altimeters
Combination of fixed and programmable attenuators achieve IPL’s

## Slide 44: Radio Altimeter Tolerance of WAIC Systems
Expanding the Test Bed
Achieving Higher Power Interference
Simple modification to altitude simulator enabled higher power interference without changing fixed/step attenuators

## Slide 45: Radio Altimeter Tolerance of WAIC Systems
Expanding the Test Bed
Adding Lower Altitude Capability
40ft coax altitude simulator used some during initial testing regimen.
95ft coax added later on

## Slide 46: Radio Altimeter Tolerance of WAIC Systems
Expanding the Test Bed
Full Test Diagram

## Slide 47: ‘In Band’ WAIC Test Results

## Slide 48: Radio Altimeter Tolerance of WAIC Systems
‘In Band’ WAIC Tests
Results Overview
Combined test setup described above used to simulate 200 MHz OFDM signals for all five altimeters
Breaking point defined as:
  Any altitude labeled NCD
  Any altitude with an absolute error greater than 2%
  Any power causing a mean altitude error greater than 0.5%
Results brought to FSMP to propose Aggregate WAIC Interference thresholds

## Slide 49: Radio Altimeter Tolerance of WAIC Systems
‘In Band’ WAIC Tests
Results – RA Type 1

## Slide 50: Radio Altimeter Tolerance of WAIC Systems
‘In Band’ WAIC Tests
Results – RA Type 2

## Slide 51: Radio Altimeter Tolerance of WAIC Systems
‘In Band’ WAIC Tests
Results – RA Type 3

## Slide 52: Radio Altimeter Tolerance of WAIC Systems
‘In Band’ WAIC Tests
Results – RA Type 4

## Slide 53: Radio Altimeter Tolerance of WAIC Systems
‘In Band’ WAIC Tests
Results – RA Type 5

## Slide 54: Radio Altimeter Tolerance of WAIC Systems
 | RA Type 1 | RA Type 2 | RA Type 3 | RA Type 4 | RA Type 5
WAIC Interference Threshold | -54 dBm | -56 dBm | -44 dBm | -56 dBm* | -44 dBm
‘In Band’ WAIC Tests
Results – Summary

## Slide 55: ‘Out of Band’ WAIC Test Results

## Slide 56: Radio Altimeter Tolerance of WAIC Systems
‘Out of Band’ WAIC Tests
Preliminary results here

## Slide 57: Conclusions

## Slide 58: Radio Altimeter Tolerance of WAIC Systems
Conclusions
Results of Test Bed Automation
Successfully developed a reference test bed validated by RA manufacturers and aircraft manufacturers.
Developed automation which enabled testing under a wide range of test conditions
Developed reporting formats which supported the development of international standards
  International Civil Aviation Organization Standard and Recommended Practices
  RTCA Inc. Minimum Aviation System Performance Standards
  RTCA Inc. Minimum Operational Performance Standards

## Slide 59: References
“Minimum Performance Standards Airborne Low-Range Radar Altimeters,” Industry Standard DO-155, Radio Technical Commission for Aeronautics, Washington, D.C., Nov. 1974.
“Compatibility Analysis Between Wireless Avionics Intra-Communication Systems and Systems in the Existing Services in the Frequency Band 4 200-4 400 MHz,” ITU Reccomendation ITU-R M.2319-0, International Telecommunication Union, Geneva, Switzerland, Nov. 2014.